## Slide 1: Week 3 Static Timing Analysis
Dr M A Raheem ECE Dept MJCET, Hyderabad
Co-Chief Investigator C2S Program at MJCET

## Slide 2: Introduction to timing path and arrival time
Timing Definition: Timing path = signal route from start point (launch flop/input port) to end point (capture flop/output port)
Start & End points:
Start: Launch flop or input port.
End: Capture flop or output port.
Arrival time: Time taken by signal to travel from start point to end point.
Required time: Latest allowable time for signal to reach endpoint to meet design constraints.
Slack: Difference between Required time and Arrival Time
Postive: meets timing
Negative: timing violation
Complex Designs: Multiple paths and endpoints make timing analysis more critical; each endpoint’s AT must be checked.

## Slide 3: Introduction to required time and slack
Quiet Time Concept: Expected time for a signal to arrive at a node; signal must arrive within a defined range.
Minimum & Maximum Expected Times:
Min Expected: Earliest allowed arrival.
Max Expected: Latest allowed arrival.
Slack Calculation: Difference between expected time (quiet time) and Actual arrival time:
Setup & Hold Slack:
Setup Slack: related to setup time requirements.
Hold Slack: related to hold time requirements.
Design Implications: Multiple paths & endpoints make slack analysis critical for STA;
ensures design meets system specifications.
Key Insight: Slack analysis identifies whether a signal arrives too early, too late, or on time relative to design expectations.

## Slide 4: Introduction to basic categories of setup and hold analysis
Edge-to-Edge Analysis: Timings from launch flop to capture flop; focuses on register-to-register paths.
Input-to-Register Analysis: Timing from input ports to flip-flops; often requires virtual clocks for analysis.
Register-to-Output Analysis: Timing from capture flop to output ports; part of IO timing analysis.
Input-to-Output Analysis: Paths from input ports to output ports; treated as separate IO timing analysis.
Clock Gating Paths: Analysis of paths affected by clock gating; ensures signals meet timing when clocks are selectively blocked.
Recovery/Reset Analysis: Timing for synchronous pins like reset; ensures signals respond correctly after a clock edge.
Grouping advantage: Categorizing timing paths allows easier and separate analysis for complex designs.

## Slide 5: Introduction to data check and latch timing
Control & Reset Signals:
Gates controlled by signals; ensures synchronous operation.
Endpoints can include control signals for timing checks.
Hold checks:
Ensure signals arrive at endpoints in correct sequence.
Checks depends on special constraints for control signals.
Latch Timing:
Flops: Edge-triggered; capture on clock edge.
Latches: Level-sensitive; transparent during clock level.
Latches can borrow time to/from flops, helping in pipelining.
Timing Paths with Latches:
Flop paths must be analyzed separately.
Latch transparency affects setup and hold timing.
Slew & Transition Analysis:
Ensures signal transitions are within min/max slew requirements.
Prevents short circuits power issues and gate timing violations.

## Slide 6: Introduction to slew, load and clock checks
Load analysis:
Measure Load at each node (capacitance) for charging/discharging.
Check against max/min permissible values to ensure reliable operation.
Important for both data paths and clock nets.
Clock timing Analysis:
Critical in static timing analysis (STA).
Two main checks:
Clock Skew: Latency differences from clock source to flops/outputs.
Must be within acceptable range; impacts setup/hold/recovery timing.
Proper skew management ensures reliable timing across all paths.
Clock pulse width:
Ensures pulse is visible at all endpoints.
Must not degrade excessively, or flops may fail to capture data.

## Slide 7: Convert logic gates into nodes
Single-Clock Circuit: Launch flop → combinational logic → capture flop; clock frequency = 1GHz.
Logic Delays: Buffer = 2 units, AND = 2 units, OR = 3units; input arrival times ~ 0.3-0.4 units.
Timing Graph (DAG): Nodes = gates /flops/inputs; edges = signal delays; converts circuits into analysable form.
Signal propagation: Example: IO → B = 0.1 units, I1 → B = 0.25 units, I3 → C = 0.2 units.
Setup Analysis Goal: Track signal arrival times across DAG and ensure constraints at capture flop are met.
Next step: Complete DAG and calculate all arrival times to check setup timing.

## Slide 8: Compute actual arrival time (AAT)
Convert the circuit into a timing graph (DAG): nodes = gates/wires, edges = delays.
Input arrival times: time from source to each input node (includes wire + gate delays).
Node delays: intrinsic gate/wire delays added to incoming path arrival times.
Actual arrival time:
Setup analysis → max arrival from all paths.
Hold analysis → min arrival from all paths.
Multiple paths: node arrival = max/min of incoming paths; propagates to output.
Timing graphs used by software to calculate arrival times,slack and timing violations.

## Slide 9: Compute required arrival time (RAT)
Required time/ OTA (Odditiy): Time at a node when the latest expected transition must occur within a clock cycle.
Calculation Difference: Actual arrival time = addition along paths; Required time = subtraction from final node back through the graph.
Multiple Inputs to a node: Choose fastest path for required time; choose slowest path for arrival time.
Slack computation: Slack = Required time – Actual arrival time; positive slack → safe, negative slack → timing violation.
Node-level analysis: Every node stores both actual arrival and required times; usednto identify critical nodes causing negative slack.
Importance: Helps in EC (Engineering Change) decisions, timing fixes and ensuring setup/hold constraints are met.

## Slide 10: Compute slack and introduction to GBA-PBA analysis
Node-level slack: Calculated for every node, not just endpoints, to identify which node contributes most to negative slack.
Improving slack: Critical nodes with negative slack can be optimized by upsizing logic or reducing delay.
Graph-based analysis: Two types –
Worst – case (GB): Considers all possible paths, worst – case delays.
Best – case /path – based (PB): Considers actual paths taken on silicon, more realistic.
Pin – level analysis: Each input/output pin can have its own slack,providing more accurate timing evaluation.
Purpose: Helps in EC decisions, timing closure and realistic timing verification for silicon implementation.

## Slide 11: Convert pins to nodes and compute AAT, RAT and slack
Pin – based timing graph: Nodes represent pins instead of cells; cell delays are retained but cells themselves are abstracted.
Building the graph: Each wire and pin becomes a node; delays from input to output pins are tracked to maintain timing accuracy.
Node arrival times: Calculated by adding delays along paths; for multiple inputs, the latest arrival time is considered (for setup analysis).
Required times & slack: Calculated in reverse from endpoints; required time at a node = required time at next node – interconnect/cell delays.
Slack evaluation at every node: Slack = required time – actual arrival time; identifies nodes with negative slack for potential optimization.
Purpose: Pin – level timing graphs allow detailed timing analysis, help identify critical paths, and guide design changes to meet timing constraints.

## Slide 12: Introduction to transistor level circuit for flops
Purpose: Introduces why we analyze launch and capture flop at the transistor level – to understand internal timing like clock to Q delay and setup/hold windows.
Clock Path Context: Explains that a 1 GHz clock (1ns period) drives the circuit, and for proper setup timing, total combinational delay + clock delays must be < 1ns.
Clock network buffers: In a realistic design, the clock passes through the multiple buffers and wires → causing clock arrival shifts (launch clock = +2 units delay, capture clock = +3 units).
Clock paths Defined:
Data path 1: From launch clock to output of launch flop → includes internal C → Q delay and buffer delays.
Data path 2: From clock root to capture flop → includes its own buffer chain and delay.
Timing Graph Impact: The shifted edges create clock skew (Δt) between launch and
capture → affects setup slack and timing closure.

## Slide 13: Negative and positive latch transistor level operation
Negative latch → active when clock = LOW; Positive latch → active when lock = HIGH.
Built using transmission gates (pass transistors) – NMOS +PMOS combinations that pass signals depending on the clock level.
The data propagation from input to output passes through ~3 elements (two logic gates + one transmission gate), defining internal setup and hold delays.
Positive latch works on the HIGH level of the clock; its structure is similar but with the clock and clock-bar signals swapped.
Both latches introduce finite delays inside a flip-flop, affecting setup/hold timing.
A flip-flop is formed by combining one negative latch + one positive latch in a master-slave configuration, ensuring edge-triggered operation.

## Slide 14: Library setup time calculation
Master-Slave FF Structure: Negative latch (master) → Positive latch (slave) forms edge-triggered flip-flop.
Negative Latch Behavior: Passes input D to QM when clock is LOW; uses transmission gates.
Positive Latch Behavior: Captures QM to Q when clock is HIGH; slave responds to positive clock level.
Setup Time: Input must be stable before clock rising edge; ensures correct data capture.
Internal Delays: Setup accounts for propagation through 3 inverters + 1 transmission gates.
Key Observations: QM holds data before clock edge; prevents data corruption during clock transition.

## Slide 15: Clk-q delay calculation
Clock to Q Delay: Time taken for data to propogate from flip-flop input to output after clock edge; determined by transmission gates and internal inverters.
Positive Clock level behavior: When clock is HIGH, certain transmission gates turn on retaining previous QM state and preparing output.
Setup time consideration: Input must be stable before clock edge; ensures reliable data capture at Q.
Hold Time: Time after clock edge during which data can change without affecting output; often zero in ideal cases.
Clock variations: Real chip clock networks can have propagation variations due to long nets and multiple gates; clock edge may not arrive exactly as intended.
Timing calculations: Realistic analysis subtracts setup/hold times from clock to Q to account for delays and variations across the network.

## Slide 16: Steps to create eye diagram for jitter analysis
Source of setup/Hold values: These values come from foundry characterization of standard cells and flip-flops; used in static timing analysis.
Clock signal Variations: Real silicon has variations in clock arrival times due to long nets and transistor-level differences; ideal zero/one edges aren’t exact.
Power supply effects: Voltage drops and IR drops across the chip introduce additional variations in clock levels and timings.
Ideogram Concept: Combines multiple versions of clock signals ( including variations) to visualize how a flip-flop behaves in real conditions; resembles an “eye” diagram.
Operating window: Ideogram helps identify the time window in which flip-flop operates reliably, accounting for all variations.
Static timing analysis usage: Ideograms and characterized values are inputs to timing reports; engineers don’t manually generate them but rely on EDA tools.

## Slide 17: Jitter extraction and accounting in setup timing analysis
Noise Margin: Range where signals are still reliably logic 0 or 1 despite distortion.
Jitter: Variations in clock edge timing that affect data capture.
Clock Uncertainity: Combined effect of jitter,skew and other variations; reduces effective clock period.
Setup time check: Data must arrive before the clock edge minus setup and uncertainity.
Next Step: Use numerical timing reports to verify setup/hold across the whole design.

## Slide 18: Setup analysis - graphical to textual representation
Graph → Text conversion: Graphical timing info (data arrival, launch/capture points) is converted to numbers in reports for industry use.
Components Represented Numerically: Each net, cell and path delay is assigned a numeric value.
Data & clock delays: Launch and capture timing calculated as Data Arrival + Delta < clock period – setup time – uncertainity.
Repeated Nets (Beaven Example): Some nets appear multiple time;. Extra pessimism is added, which is later optimized (handled in OCV/CERP).
Textual Representation Purpose: Makes it easier to compute slack, setup violations, and validate timing for entire design.
Next step: Combine all individual textual calculations to full-chip setup analysis and prepare to CERP/OCV adjustments.

## Slide 19: Hold analysis with real clocks
Hold time Definition: Minimum time after a clock edge that the data must remain stable at the input of the capture flop.
Hold vs. Setup: Setup = data arrives before clock egde; Hold = data must stay stable after clock edge.
Launch & capture flops: Hold analysis mainly depends on the launch flop timing; data must not change too early.
Uncertainity & Jitter: Clock edge variations are added to ensure hold constraint are met. Hold uncertainity is usually smaller than setup uncertainity.
Holding Time Equation: Data Arrival Time ≥ Launch Edge + Hold Time + Uncertainty
Graphical → textual conversion: just like setup analysis, hold timing diagrams are converted to numerical form for reports and verification in real designs.

## Slide 20: Hold analysis - graphical to textual representation
Launch path equation: Data arrival time = clock (Launch path delay) + Data path delay
Capture path equation: Data required time = clock (capture path delay) + hold time + uncertainity.
Hold analysis focus: Uses minimum delay values instead of max, to detect early data arrival.
Common path pessimism removal (CPPR): Since launch and capture clocks share common network paths, CPPR removes double-counted delay pessimism for accuracy.
Slack calculation: Hold slack = Data required time – Data arrival time.

## Slide 21: Sources of variation - etching
Etching process defines the transistor’s physical structure — its width, length, and height.
Any imperfection in etching distorts transistor geometry, especially at the edges of the wafer.
These distortions cause variation in W/L ratios, altering transistor drive current (Ids).
Changes in Ids lead to timing delays and affect signal propagation across the chip.
Middle transistors are usually more uniform; edge transistors show higher variations.
Such process-induced variations must be considered in Static Timing Analysis (STA) to ensure realistic results.

## Slide 22: Sources of variation - oxide thickness
Oxide thickness variation occurs in the gate oxide layer of MOS transistors during fabrication — it’s supposed to be uniform, but real oxidation processes cause uneven thickness.
The thickness of the gate oxide (tox) directly affects oxide capacitance (Cox) — thinner oxide → higher capacitance → higher drain current (Ids).
Non-uniform oxide → inconsistent Ids across transistors → timing variation in inverters and logic paths.
Edge transistors experience more oxide thickness variation than center transistors, due to uneven fabrication conditions.
Result: Thicker oxide = lower Ids = slower switching, thinner oxide = higher Ids = faster switching, leading to timing skew in circuits.

## Slide 23: Relationship between resistance, drain current and delay
Propagation delay (tpd) in a circuit depends mainly on resistance (R) and capacitance (C) — larger R or C → longer delay.
In MOSFETs, resistance is not constant like in Ohm’s law — it varies nonlinearly with drain current (Ids) and drain-to-source voltage (Vds).
Higher resistance = slower charging/discharging of load capacitance → increased delay; lower resistance → faster switching.
Since R ∝ 1/Ids, and Ids depends on oxide thickness (tox), W/L ratio, and process variations, these parameters directly cause delay variations.
Process variation across the chip causes inverters designed for identical delays (e.g., 100 ps) to actually show a spread (e.g., 91–108 ps) due to these differences
The distribution of such delays is represented by the On-Chip Variation (OCV) curve, and this variation data is used in Static Timing Analysis (STA) for accurate timing verification..

## Slide 24: OCV based setup timing analysis
OCV (On-Chip Variation) means even identical cells on the same chip show different delays due to fabrication/process variations (e.g., ±20%).
During setup timing analysis, OCV is modeled by modifying delays by a certain percentage (e.g., ±20%) in different timing paths.
Pulling in the clock (reducing delays by 20%) results in a more realistic and conservative analysis since it simulates worst-case setup timing (less margin).
Example effect: When clock path cells are pulled in by 20%, slack reduces (e.g., from +0 ps to –20 ps) — meaning circuit speed must drop (e.g., 1 GHz → ~950 MHz).

## Slide 25: Setup timing analysis after pessimism removal
In OCV setup timing, a cell common to both launch and capture paths (like B1) was showing two different delays simultaneously — which is physically impossible.
A single cell can have only one delay value at a given instant, either typical or OCV-modified, not both.
This duplicate consideration adds extra pessimism (overestimation of delay), roughly 25.6 ps in the example given.
To fix this, we remove the extra pessimism from the total delay calculation of the common clock path.
After adjusting, the required time increases, and the slack turns positive, meaning the circuit can safely operate at 1 GHz again.

## Slide 26: OCV based hold timing analysis
Hold analysis checks if the data is too fast and captured by the next clock edge too early — crucial for circuit stability.
Under OCV (On-Chip Variation), both data and clock delays can change by ±20%, affecting hold margins
For worst-case hold, engineers apply clock pull-in and clock push-out — pulling in launch clock (reducing delay) and pushing out capture clock (increasing delay)..
This makes the analysis more conservative, ensuring stability even under extreme variation conditions.
If a negative slack appears during hold analysis, it indicates a hold violation, which can cause metastability or timing failure.

## Slide 27: Hold timing analysis after pessimism removal
In hold analysis, launch clock is pulled in (−20%) and capture clock is pushed out (+20%) to model worst-case variation.
This makes the hold slack more negative, revealing possible hold violations (in this case ≈ −39.6 ps).
Such violations cause unreliable data capture or metastability, so they must be caught before fabrication.
Common clock sections between launch and capture paths can introduce extra pessimism if counted twice.
The difference in delay (≈ 51 ps) between these shared sections is corrected using Clock Path Pessimism Removal (CPPR).
After removing this excess delay, the slack turns positive (≈ +16 ps) — confirming the design now meets hold timing safely.